Records

Records will be kept of:

- Contractors safety information

- Risk assessments undertaken

- Inspections and tests (detailing date tested, name of tester and date of next test) plus details of any modifications or repairs made

- Personal protective equipment required

- Information and training provided

Signature:   ……………………………………………………

Position:	 Director

Date: 30/04/21

Review: 01/05/22

# Text boxes

Page 1 of 3

Suitable precautions will be taken where there are interruptions to the electrical continuity, or where

high impedance is introduced, to a referenced circuit conductor (i.e. circuit conductor connected to

earth or some other reference point) that may give rise to danger.

Integrity of Referenced Conductors

Suitable precautions will be taken to prevent danger where it is foreseeable that conductive materials

may become electrically charged, either as a result of the use of an electrical system, or as a result of a fault.

Earthing or Other Suitable Precautions

All electrical conductors in a system that may give rise to danger will be either suitably insulated o r

other precautions taken to prevent danger.

Insulation, Protection and Positioning of Conductors

All electrical systems will be constructed and maintained so as to prevent danger at all times, so far as

is reasonably practicable.

Mains must be maintained by the client/user as part of their periodic inspections.

Work activities including the operation, use and maintenance of a system and any work near a system

will be carried out in such a way as not to give rise to danger.

Clymac Ltd will ensure that any personal protective equipment will be suitable for its intended use, well maintained and properly used.

Systems, Work Activities and Protective Equipment

A suitable and sufficient risk assessment of the risks arising from any work activity that might expose

any persons to danger from electricity will be undertaken for the purpose of identifying all necessary measures required to reduce any risks found as a result of the assessment.

Evaluation and Risk Assessment

Arrangements

Clymac Ltd recognises that the installation, final connection and maintenance   of fire alarm mains

supplies can be hazardous and will ensure all reasonable steps are taken to reduce the risks, as far as is possible.

Policy

Health and Safety at Work Act

Consumer Protection Act

Electricity at Work Regulations

Electrical Equipment (Safety) Regulations

Relevant Legislation

Safe Isolation & Procedure Policy

Page 2 of 3

Where appropriate, all persons who carry out electrical work will be competent to do so or will be

adequately supervised.

Persons carrying out work on electrical equipment, circuits or installations will be provided with appropriate information and instruction relating to safety aspects of the electrical equipment.

Users of portable and transportable equipment will be trained to check before use for visible defects

to plugs and leads, etc.

Information and Training

Adequate working space, adequate means of access and adequate lighting will be provided at all

electrical equipment on which electrical work is being done which may give rise to danger.

Working Space, Access and Lighting

Live working (including fault finding and testing) will  NOT be undertaken unless it is unreasonable to

isolate the conductors from sources of energy and unless it is reasonable (absolutely necessary) to

carry out the work ‘live’ and suitable precautions are taken e.g testing output from a mains supply.

Work on or Near Live Conductors

class and type of equipment

environment in which it is used frequency of use

•

•

•

All electrical systems will be maintained so as to prevent, so far as is reasonably practicable, danger.

This will be achieved by carrying out routine safety testing, and where practicable, visual inspections at appropriate intervals. Any defects should be noted in the engineer report and passed on to the relevant staff.

The frequency of inspections and testing will vary according to the likelihood of dangerous faults occurring and will be determined by considering the following factors:

Maintenance

Adequate precautions will be taken to prevent ‘dead’ equipment which is electrically isolated or

switched off from becoming electrically charged to prevent danger while work is carried out on or

near that equipment.

Precautions for Work on Equipment Made Dead

Where necessary to prevent danger, suitable means will be available for cutting off the supply of

electrical energy to any electrical equipment and for the isolation of electrical equipment. A lock off

kit will be supplied and used and once isolated if possible any access to the isolated circuit will be locked.

Means for Cutting off the Supply and for Isolation

All joints and/or connectors, whether temporary or permanent, used in an electrical system, will be

mechanically and electrically suitable for that use so as to prevent danger.

Connection